HOTEL CORPORATION OF INDIA LTD.,

IGI Airport, Terminal-2

New Delhi‐110037.

# Public Tender Notice

| Tender No. | Name of Work | Last date For submission |
| --- | --- | --- |
| DEL/02/2016-17 Dtd.3.5.2016 | Repair of cooling tower tank leaks at Centaur Hotel, IGI Airport, New Delhi. Estimated value : Rs.15.34 Lacs. | 8.06.2016 |

For further details regarding tender documents, please visit our website http://www.centaurhotels.com. Amendments (if any) shall be hosted on HCIL website 07 days prior to opening of the tender and no separate intimation for amendment/extension shall be published in the newspapers.

s/d

Sr.Asst. Manager (Purchase)

HOTEL CORPORATION OF INDIA LTD.,

IGI Airport, Terminal-2

New Delhi‐110037.

##### Tender No. DEL/02 /2016-17	Dated: 03.05.2016 ,   Due Date: 08.06.2016

##### Sub: Inviting quotations for Repair of Cooling Tower Tank Leaks at  Centaur Hotel, IGI Airport, New Delhi.  Estimated Tender value : Rs. 15.34 Lacs  approx.

## TENDER DETAILS

Sealed / closed  tenders are invited by “Hotel Corporation of India Limited” here after termed as “HCIL” from prospective bidders under two bid system  that is Technical Bid : Part-A and Financial Bid : Part-B for the subject services. The bidders fulfilling Technical eligibility criteria of this Tender may apply as per following documents : -

## 1.0 	1.0 Tenderers are requested to submit their quotations as per following documents :

| S.No. | Particulars | Annexure |
| --- | --- | --- |
| 1.1 | Specifications and other details | I |
| 1.2 | Technical Bid Form- Part A. | II |
| 1.3 | Price Bid Form -Part B | III |
| 1.4 | Certificate for unconditional acceptance of Terms & Conditions of the tender. | IV |
| 1.5 | Details of Contract | V |

2.0 	METHOD OF SUBMISSION OF QUOTATIONS IN TWO BID SYSTEM

2.1	ENVELOPE ONE - shall contain  duly filled “Technical Bid - Part A ’ together with EMD and supporting documents. The envelop should be superscribed with: ENVELOPE ONE  – “Technical Bid- Part A” for “Tender No. DEL/02/2016-17, dated : 03.05.2016 Due Date: 08.06.2016. Name of the Tenderer / Co.  and address to be written at the bottom of envelope for identification.

2.2   ENVELOPE TWO : shall contain duly filled “Price Bid Form – Part B” .The envelop should be superscribed with ENVELOPE TWO - “Price Bid – Part B”  Tender No. DEL/02/2016-17, dated : 03.05.2016,  Due Date: 08.06.2016. Name of the tenderer / Co.  and Address to be written at the bottom of envelope for identification. The Price Bid must be signed by your authorized representative bearing Company Stamp.

Note :  The tenderer(s) may use “HCIL” Tender Documents for applying to this tender  and must put their Co’s Stamp on each page duly signed by the Authorized signatory of the Tenderer / Co. For submission of Price Bid, Tenderer can use their Company letter head for submission of Bid but in this case, it has to be typed in the manner / format shown in our “Price Bid Form- Part B”.

Contd……2/-

Page 2

Annexure I

  - ENVELOPE THREE (MASTER ENVELOPE) : The above two sealed / closed envelopes (Envelope One and Envelope Two) must be put in the “Third / Master Envelope” which should be superscribed with “Quotation for Tender No. DEL/02/2016-17, dated:

03.05.2016, Due Date:08.06.2016 at 1530 hrs ”.  Name of the tenderer / Co.  and Address to be written at the bottom of envelope for identification. The tenders should be submitted at the Corporate Purchase Tender Box  kept at Security Department, Centaur Hotel, IGI Airport, New Delhi-110037 on or before 1500 hrs. of 08.06.2016 No bids will be entertained after the stipulated time.

3.0 	The perspective Tenderers / bidders may send their offer in sealed/closed envelope  so as to reach us at above mentioned address on or before 08.06.2016 .by 1500 hrs.

4.0 	The tender closes on 08.06.2016 at 1500 hrs. The closing date may be extended at the sole discretion of ‘HCIL’.

5.0 	The Technical Bids shall be opened on the due date /time of the tender.

6.0 	Tenderers who wish to attend tender opening may do so OR send their representative with authorization letter on their Company’s letterhead signed by their authorized signatory which should be produced at the time of opening of tender at above address/time.

7.0	‘HCIL’ reserves the right to reject any tender in part or full or annual the tender process without assigning any reason.

8.0  	The Commercial Bids of only technically suitable vendors will be opened thereafter.

Sd/-

Sr. Asst. Manager - Purchase

(Corporate Purchase)

Annexure I

HOTEL CORPORATION OF INDIA LTD.,

IGI Airport, Terminal-2

New Delhi‐110037.

##### Tender No. DEL/02 /2016-17	Dated: 03.05.2016 ,   Due Date: 08.06.2016

Specification for repair of Cooling Tower Tank leaks, CHDA.

| S. No. | Description | Qty. | Unit | Rate (Rs./Unit) | Amount (Rs.) |
| --- | --- | --- | --- | --- | --- |
| 1 2 3 4 | Dismantling old plaster or skirting raking our joints and cleaning the surface for water proofing and plaster including disposal of rubbish to the dumping ground within 50 meters load 15.56 Providing and laying water proofing treatment in vertical and horizontal surface of sump (of cooling tower) by applying cement slurry mixed with water proofing cement compound consisting of applying a) first layer of slurry cement @ 0.488 kg/sq.m mixed with water proofing cement compound @ 0.253 kg/sq.m. This layer will be allowed to cure for 4 hours. b) second layer of slurry of cement @ 0.242 kg/sq.m mixed with water proofing cement compound @ 0.126 kg/sq.m. This layer will be allowed to cure for 4 hours followed with water curing for 48 hours. The rate includes preparation of surface, treatment and sealing of all joints, holes, opening, corners, junctions of pipes and masonry with polymer mixed slurry 22.5 Supply & Fixing/applying 12 MM cement plaster of mix 1:4 (1 cement: 4 fine sand) Providing and fixing double scaffolding system (cup lock type) on the exterior side, upto seven story height made with 40 MM dia M.s. tube center to center , horizontal and vertical tubes joining with cup and lock system with M.S. clamps, and MS stair case system in the scaffolding for working platform etc. and maintaining it in a serviceable condition for the required duration as approved and removing thereafter. The scaffolding system shall be stiffened with bracings, runners, connection with the building etc. wherever required for inspection of work at required locations with essential safety features for the workmen etc. complete as per the directions and approval of Engineer-in-Charge. The elevational area of the scaffolding shall be measured for payment purpose. The payment will be made once irrespective of the duration of scaffolding 17.72 or similar padding/scaffolding with wooden ballies. Note: Taxes extra as applicable | 1756 1357 1756 4297 | Sq.M Sq.M Sq.M Sq.M |  |  |

Terms & Conditions:

- Statutory deductions for ESI, PF, IT etc. will be done from the bills.

- Payment: 95% of Running Bills of Rs.2,00,000/- of more will be paid. 5% will be paid after completion of defects liability period of one year.  During the defect liability period of one year all defective materials to be repaired/replaced free of cost by the contractor.

- Rates to be inclusive of all tools, tackle, materials, scaffolding, ladders, hand lamps etc.  complete as required for satisfactory job completion.

- Work to be completed within a period of 150 days from the date of receipt of PO otherwise a penalty @ 0.5% per week subject to maximum 5% will be deducted from the bill of the non completed portion of the work.

- Prequalification Criteria: The Contractor should have carried out during the last 5 years

- One  job of 80% value of estimated cost

OR

- Two  jobs of 50% value of estimated cost

OR

- Three  jobs of 40% value of estimated cost

AND

- The contractor should have average annual turnover of 30% of estimated cost during the last three years.

- Rates to be inclusive of fixing suitable dummies (and removing after completion of work) if pipe line valves are not holding.

- All quantities given are approximate. Measurement and payment will be done on actual completed work.

- Shutdown to be taken in coordination with Engineering Department.

HOTEL CORPORATION OF INDIA LTD.,

IGI Airport, Terminal-2, New Delhi‐110037.

ANNEXURE- II

#### TECHNICAL BID FORM – PART A

##### Tender No. DEL/02 /2016-17	Dated: 03.05.2016,         Due Date: 08.06.2016

##### Sub: Inviting quotations for Reair oof cooling tower tank leaks at Centaur Hotel, IGI Airport, New Delhi.  Estimated  value Rs. 15.34 lac.

| 1. | Name of the Bidder / Co. |  |
| --- | --- | --- |
| 2 | Complete Address of the bidder/Co. |  |
| 3 | Telephone No. / Mobile No./ Fax No. /email ID |  |
| 4 | Name of Contact Person & mobile. |  |
| 5. | Whether copy of address proof enclosed such as latest electricity bill/ Water bill/ House tax receipt/Rent agreement/MOU etc. of bidder / Co. (Must) | Yes / No |  |
| 6. | Whether EMD of Rs.7500/- enclosed. . (Must) | Yes/No | DD/Cash Receipt No. …… Date…………………. |
| 7. | Registration with Govt./Semi Govt. Organisation, if any. | Yes/No |  |
| 8. | Latest Solvency Certificate from a Nationalized Bank/Schedule Bank | Yes/No |  |
| 9. | Income Tax Permanent Account Number. | Yes/No |  |
| 10. | List of works carried out, value of such completed works and certificate for work executed/under successfully completed similar works during last five years. | Yes / No |  |
| 11 | Contractors who have successfully completed similar work during last five years ending 31.3.2015 as detailed below, only shall be considered for the evaluation of the technical bid. | Yes / No |  |
| 11(a) | Three similar completed works costing not less than then the amount equal to 40% of the estimated cost (OR) | Yes / No |  |
| . 11(b) | Two similar completed works costing not less than the amount equal to 50% of the estimated cost (OR) | Yes/No |  |

Contd..2/-

Page:2

ANNEXURE- III

| 11 ( c) | One similar completed work costing not less than the amount equal to 80% of the estimated cost. | Yes/No |  |
| --- | --- | --- | --- |
| 12. | Whether having an average turnover of Rs.5.00 Lacs per year for last 03 Fin yrs i.e. 2012-13, 13-14 & 14-15. (Must) |  |  |
| 13. | Whether Self Certified copy of Balance Sheet, Profit and loss account duly verified by Regd. Chartered Accountant enclosed in support.of above. | Yes/No | 2012-13 2013-14: 2014-15: |
| 14 | Whether self attested copy(s) of Income Tax Returns for last 03 Financial years - . 2012-13, 13-14 & 14-15 enclosed. | Yes/No | 2012-13: 2013-14: 2014-15: |
| 15 | Whether Certificate for unconditional acceptance of all the terms and conditions of the tender on the Bidder’s letter head enclosed as per format (Annexure-I). (Must) | Yes/No |  |
| 16. | Whether details of institutional Customers enclosed.(Optional ) | Yes/No |  |
| 18. | Are you already doing business with HCI or any of HCI Units in your or under some other name? If so, what name? | Yes/No |  |
| 19 | Has your company been Black Listed by any agency of the Airport or else where. If yes, please give details. | Yes / No | If yes, details. ……………… |

Signature of authorized signatory     ………………………………………

Name of authorized signatory……………………………

Name of the company……………………..

Company’s Seal………………………………

Date ……………………

Place…………………………

HOTEL CORPORATION OF INDIA LTD.,

IGI Airport, Terminal-2,New Delhi‐110037.

Annexure:III

FINANCIAL BID FORM

##### Tender No. DEL/02 /2016-17      dated: 03.05.2016 ,        .Due Date : 08.06.2016

##### Sub: Inviting quotations for Reair oof cooling tower tank leaks at Centaur Hotel, IGI Airport, New Delhi.  Estimated  value Rs. 15.34 lac.

| SN | Description |  |
| --- | --- | --- |
| 1 | Name of the bidder’s Co./ Firm / Establishment |  |
| 2 | Full Address of Registered Office |  |
| 3 | Telephone No./ Mobile Tel No/ Fax No. |  |
| 4 | Name of Contact Person |  |
| 5. | Financial offer : |
| Rates for Reair oof cooling tower tank leaks at Centaur Hotel, IGI Airport, New Delhi. Estimated value Rs. 15.34 lac. |
| (i) | Rate Rs. …………for complete work. | Rs. ….. … per Month |
| 6. | L-1 Criteria | L-1,bidder will be decided based on lowest rates quoted above. |

7.	Inclusion and exclusion /Govt. taxes and levies applicable to quoted rates :

a)	Inclusions:

The rates quoted above are  inclusive of Capital Cost including equipments, Manpower cost, Government Taxes and levies and all statutory payments like ESI / PF etc.

b) 	Exclusions:

- The Service Tax (including education cess)  applicable  on quoted rates is excluded.“ service tax  , if applicable,  would be paid / reimbursed separately as per the prevailing rates,  on submission of receipt as proof for payment together with monthly bills.

Contd..2/-

Page:2

ANNEXURE- III

8.	Rates quoted above are valid for 120 days from the date of opening of technical bids for consideration of HCIL.

9.	It is confirmed that that I am authorized to sign the tender document

Signature of authorized signatory     ………………………………………

Name of authorized signatory……………………………

Name of the company……………………..

Company’s Seal………………………………

Date ……………………

Place…………………………

********

HOTEL CORPORATION OF INDIA LTD.,

IGI Airport, Terminal-2,New Delhi‐110037.

ANNEXURE –IV

PERFORMA FOR C E R T I F I C A T E FOR UNCONDITIONAL ACCEPTANCE OF TERMS & CONDITIONS OF THE TENDER (TO BE SUBMITTED WITH TECHNICAL BID- PART A) ON TENDERER’S LETTER HEAD)

To,

The Sr. Asst. Manager – Purchase,

Corporate Purchase Section,

Hotel Corporation of India Ltd,

Centaur Hotel, IGI Airport Terminal -2,

New Delhi -110037

Dated:…………….

Dear Sir,

##### Sub:  C e r t i f i c a t e for unconditional acceptance of terms & conditions, specifications  of the Tender No. DEL/02 /2016-17	Dated: 03.05.2016,   Due Date: 08.06.2016 Sub: Inviting quotations for Reair oof cooling tower tank leaks at Centaur Hotel, IGI Airport, New Delhi.  Estimated  value Rs. 15.34 lac.

It is certified that we have studied and understood the contents of the above referred tender documents and hereby agree for the terms and conditions and specifications  of the  subject Tender issued by “HCIL”.

Signature of authorized signatory     ………………………………………

Name of authorized signatory……………………………

Name of the company……………………..

Company’s Seal………………………………

Date ……………………

Place…………………………

HOTEL CORPORATION OF INDIA LTD.,

IGI Airport, Terminal-2,New Delhi‐110037.

Annexure: V

##### Sub: Inviting quotations for Reair of cooling tower tank leaks at Centaur Hotel, IGI Airport, New Delhi.  Estimated  value Rs. 15.34 lac.

##### Details of Contracts in support of 03 years Experience after 31.3.2016

| SN | Name of Contract | Name & Address of the Customer | Period of Contract | Value of contract In Rs. | Performance Certificate From user attached. Yes/No | Remarks |
| --- | --- | --- | --- | --- | --- | --- |
|  |  |  | From | To |  |  |  |

Notes: The Tenderer must enclose self attested copy(s) of the contracts and at least one Performance Certificate (mentioning contract details and value) issued by the Customer/ user .

a)	I hereby confirm that I am authorized to sign the tender document.

b) 	I hereby confirm that the information given above is true and correct to the best of my knowledge and belief and nothing material is concealed.

Signature of Auth Signatory : ………………………………..

Name of Auth Signatory : ………………………………..

Designation of Auth Signatory : ………………………………

Co.’s Name & Seal : ………………………………..

Place ; New Delhi.

Date……………..

***********